## Slide 1: Industrial Engineering Assignment Part 1
Prof. Dr. Dr.-Ing. Yilmaz Uygun

## Slide 2: Groups
Form a group with a maximum of 5 members
Sign up for the groups by April 10, 2022
    https://docs.google.com/spreadsheets/d/1CsBZFyeaVxg2B7wVugczel22fUtt_HL0hxua87Ja_Ig/edit?usp=sharing
The bonus assignments consists of two parts
    A succesfull submission (i.e. proper completion of all task of both parts of the assignments) will result in a bonus of 5%
TA´s office hours: Mondays at 09:45 in MS Teams; additionally on
  Tuesday, April 19th at 12:30-13:30
  Wednesday at 12:30-13:30

## Slide 3: E-scooter Production

## Slide 4: Assignment Part 1
Introduction
  Gather background and basic information on e-Scooters and present them
Strategic Planning
  Find at least 3 possible locations in Germany where you would like to start your business and select the optimal one
  Develop a production morphology for your e-Scooter production
Product Development
  Analyze customer requirements by using the House of Quality
  Create a bill of materials for your e-Scooter
Process Planning
  Conduct an ABC analysis of your products to come up with the A products
  Define the product clusters by using the routings
Materials
  Define the materials for the specific components of your e-scooter
  Consider the requirements for those components
  Discuss the forces on those components and the affected properties of the materials for those components
  Which testing method would you use to test the material properties of the components of your e-scooter?
Engineering Drawing
  Prepare a 2D (catalogue) drawing of your e-Scooter (you can draw with pencil and paper and scan it afterward)
    Front and top view (in 1st or 3rd angle & appropriate scale)
    Add and fill the title block
    Bonus: Right side view & Left side view
    Bonus: Drawing the whole e-Scooter

## Slide 5: Assignment Part 1
Complete the tasks manually by using the templates in this deck and do not use the Excel formulas
Give always brief explanations of your procedure & calculations
Written report with figures, etc. (15-20 pages)
Deadline: April 24, 2022 at 23:59
E-Mail: y.uygun@jacobs-university.de
File name: IEM_Assignment01_GroupXX.xlsx (IEM_Assignment01_GroupXX.pdf)

## Slide 6: Tables –Work stations
Work Station | WS Type | # | Setup Time [min] | Length [mm] | Width [mm]
WS-01 | MIL-AB-361 | 3 | 30 | 2000 | 1000
WS-02 | TUR-B2-362 | 3 | 30 | 2000 | 1200
WS-03 | MIL-A31-363 | 2 | 30 | 2500 | 1000
WS-04 | TUR-A4-364 | 3 | 40 | 3000 | 1200
WS-05 | MIL-A2-365 | 6 | 30 | 2200 | 1400
WS-06 | TUR-C1-366 | 2 | 40 | 2200 | 1400
WS-07 | TUR-C2-367 | 4 | 35 | 2600 | 1500
WS-08 | MIL-10-150-401 | 3 | 30 | 2000 | 900
WS-09 | TUR-20-120-402 | 2 | 30 | 2000 | 1000
WS-10 | TUR-20-180-403 | 0 | 45 | 1500 | 1000
WS-11 | TUR-40-100-404 | 2 | 20 | 1500 | 1800
WS-12 | TUR-15-250-405 | 1 | 25 | 1850 | 1650
WS-13 | TUR-6-Sp1-406 | 1 | 20 | 3000 | 1200
WS-14 | TUR-6-Sp2-407 | 0 | 30 | 2500 | 2000
WS-15 | TUR-6-Sp3-408 | 1 | 40 | 3000 | 1400
WS-16 | TUR-6-Sp4-409 | 1 | 30 | 2800 | 1500
WS-17 | MIL-H1-601 | 2 | 30 | 2500 | 1600
WS-18 | MIL-V2-602 | 2 | 30 | 2400 | 1600
WS-19 | MIL-V31-603 | 2 | 30 | 2400 | 1600
WS-20 | MIL-H21-604 | 3 | 20 | 3000 | 2500
WS-21 | MIL-U1-605 | 2 | 30 | 3500 | 2600
WS-22 | MIL-H2-606 | 1 | 42 | 3000 | 2500
WS-23 | MIL-U2-607 | 3 | 35 | 2800 | 2000
WS-24 | MIL-V5-608 | 7 | 25 | 3000 | 2500
WS-25 | DR-2A-201 | 4 | 30 | 2000 | 2000
WS-26 | DR-2A2-202 | 5 | 30 | 1800 | 1500
WS-27 | GR-T1-203 | 4 | 30 | 1900 | 2500
WS-28 | DR-T3-204 | 2 | 30 | 2500 | 2500
WS-29 | GR-T11-250 | 3 | 20 | 2200 | 2200
WS-30 | DR-3A-206 | 2 | 30 | 2400 | 2400
WS-31 | DR-3AW-207 | 3 | 30 | 2000 | 2000
WS-32 | SAW-30-150-251 | 5 | 40 | 3000 | 2500
WS-33 | SAW-50-150-252 | 7 | 30 | 3000 | 2500
WS-34 | SAW-30-160-252 | 5 | 35 | 3000 | 2000
WS-35 | SAW-35-100-254 | 2 | 32 | 2800 | 2500
WS-36 | SAW-10-421 | 3 | 40 | 1500 | 1500
WS-37 | SAW-50-422 | 1 | 30 | 1500 | 1500
WS-38 | SAW-150-423 | 2 | 35 | 1600 | 1600
WS-39 | SAW-400-424 | 1 | 40 | 1700 | 1700
WS-40 | SAW-CNC-40-425 | 2 | 40 | 1700 | 1700
WS-41 | SAW-CNC-60-425 | 1 | 30 | 1500 | 1600
WS-42 | TEMP-A01-202 | 1 | 60 | 9000 | 9000
WS-43 | RAW-MAT-INV | 1 | 1 | 15000 | 25000
WS-44 | FIN-GOOD-INV | 1 | 1 | 15000 | 25000

## Slide 7: Tables - Operations
Item ID | OP | Work Station | WS Type | Execution Time [s] | Lot Size
B-001 | 30 | WS-08 | MIL-10-150-401 | 600 | 150
B-001 | 40 | WS-20 | MIL-H21-604 | 480 | 150
B-001 | 50 | WS-26 | DR-2A2-202 | 180 | 150
B-001 | 60 | WS-32 | SAW-30-150-251 | 720 | 150
B-001 | 20 | WS-36 | SAW-10-421 | 120 | 150
B-001 | 70 | WS-42 | TEMP-A01-202 | 300 | 150
B-001 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-001 | 80 | WS-44 | FIN-GOOD-INV | 0 | 150
B-002 | 30 | WS-08 | MIL-10-150-401 | 900 | 150
B-002 | 40 | WS-20 | MIL-H21-604 | 480 | 150
B-002 | 50 | WS-26 | DR-2A2-202 | 240 | 150
B-002 | 60 | WS-32 | SAW-30-150-251 | 720 | 150
B-002 | 20 | WS-36 | SAW-10-421 | 120 | 150
B-002 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-002 | 70 | WS-44 | FIN-GOOD-INV | 0 | 150
B-003 | 30 | WS-08 | MIL-10-150-401 | 600 | 150
B-003 | 40 | WS-20 | MIL-H21-604 | 480 | 150
B-003 | 50 | WS-26 | DR-2A2-202 | 300 | 150
B-003 | 60 | WS-32 | SAW-30-150-251 | 600 | 150
B-003 | 20 | WS-36 | SAW-10-421 | 120 | 150
B-003 | 70 | WS-42 | TEMP-A01-202 | 300 | 150
B-003 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-003 | 80 | WS-44 | FIN-GOOD-INV | 0 | 150
B-004 | 30 | WS-08 | MIL-10-150-401 | 480 | 150
B-004 | 40 | WS-32 | SAW-30-150-251 | 600 | 150
B-004 | 20 | WS-36 | SAW-10-421 | 120 | 150
B-004 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-004 | 50 | WS-44 | FIN-GOOD-INV | 0 | 150
B-005 | 30 | WS-04 | TUR-A4-364 | 600 | 150
B-005 | 40 | WS-20 | MIL-H21-604 | 480 | 150
B-005 | 50 | WS-31 | DR-3AW-207 | 300 | 150
B-005 | 60 | WS-32 | SAW-30-150-251 | 600 | 150
B-005 | 20 | WS-40 | SAW-CNC-40-425 | 120 | 150
B-005 | 10 | WS-42 | TEMP-A01-202 | 300 | 150
B-005 | 70 | WS-44 | FIN-GOOD-INV | 0 | 150
B-006 | 30 | WS-02 | TUR-B2-362 | 600 | 150
B-006 | 40 | WS-18 | MIL-V2-602 | 480 | 150
B-006 | 50 | WS-29 | GR-T11-250 | 300 | 150
B-006 | 60 | WS-33 | SAW-50-150-252 | 600 | 150
B-006 | 20 | WS-40 | SAW-CNC-40-425 | 120 | 150
B-006 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-006 | 70 | WS-44 | FIN-GOOD-INV | 0 | 150
B-007 | 30 | WS-02 | TUR-B2-362 | 360 | 150
B-007 | 40 | WS-18 | MIL-V2-602 | 360 | 150
B-007 | 50 | WS-29 | GR-T11-250 | 360 | 150
B-007 | 60 | WS-33 | SAW-50-150-252 | 180 | 150
B-007 | 20 | WS-40 | SAW-CNC-40-425 | 120 | 150
B-007 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-007 | 70 | WS-44 | FIN-GOOD-INV | 0 | 150
B-008 | 30 | WS-02 | TUR-B2-362 | 540 | 150
B-008 | 40 | WS-18 | MIL-V2-602 | 840 | 150
B-008 | 50 | WS-29 | GR-T11-250 | 300 | 150
B-008 | 60 | WS-33 | SAW-50-150-252 | 180 | 150
B-008 | 20 | WS-40 | SAW-CNC-40-425 | 120 | 150
B-008 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-008 | 70 | WS-44 | FIN-GOOD-INV | 0 | 150
B-009 | 30 | WS-03 | MIL-A31-363 | 540 | 150
B-009 | 40 | WS-18 | MIL-V2-602 | 360 | 150
B-009 | 50 | WS-29 | GR-T11-250 | 360 | 150
B-009 | 20 | WS-40 | SAW-CNC-40-425 | 120 | 150
B-009 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-009 | 60 | WS-44 | FIN-GOOD-INV | 0 | 150
Item ID | OP | Work Station | WS Type | Execution Time [s] | Lot Size
B-010 | 30 | WS-02 | TUR-B2-362 | 360 | 150
B-010 | 40 | WS-18 | MIL-V2-602 | 420 | 150
B-010 | 50 | WS-29 | GR-T11-250 | 420 | 150
B-010 | 60 | WS-33 | SAW-50-150-252 | 180 | 150
B-010 | 20 | WS-40 | SAW-CNC-40-425 | 120 | 150
B-010 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-010 | 70 | WS-44 | FIN-GOOD-INV | 0 | 150
B-011 | 30 | WS-02 | TUR-B2-362 | 360 | 150
B-011 | 40 | WS-18 | MIL-V2-602 | 420 | 150
B-011 | 50 | WS-29 | GR-T11-250 | 420 | 150
B-011 | 60 | WS-33 | SAW-50-150-252 | 180 | 150
B-011 | 20 | WS-40 | SAW-CNC-40-425 | 120 | 150
B-011 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-011 | 70 | WS-44 | FIN-GOOD-INV | 0 | 150
B-012 | 30 | WS-05 | MIL-A2-365 | 600 | 150
B-012 | 40 | WS-25 | DR-2A-201 | 1140 | 150
B-012 | 50 | WS-27 | GR-T1-203 | 720 | 150
B-012 | 60 | WS-32 | SAW-30-150-251 | 360 | 150
B-012 | 20 | WS-02 | TUR-B2-362 | 120 | 150
B-012 | 70 | WS-42 | TEMP-A01-202 | 300 | 150
B-012 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-012 | 80 | WS-44 | FIN-GOOD-INV | 0 | 150
B-013 | 30 | WS-05 | MIL-A2-365 | 920 | 150
B-013 | 40 | WS-25 | DR-2A-201 | 360 | 150
B-013 | 50 | WS-27 | GR-T1-203 | 360 | 150
B-013 | 60 | WS-32 | SAW-30-150-251 | 540 | 150
B-013 | 20 | WS-02 | TUR-B2-362 | 120 | 150
B-013 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-013 | 70 | WS-42 | TEMP-A01-202 | 720 | 150
B-013 | 80 | WS-44 | FIN-GOOD-INV | 0 | 
B-014 | 30 | WS-11 | TUR-40-100-404 | 600 | 150
B-014 | 40 | WS-21 | MIL-U1-605 | 540 | 150
B-014 | 50 | WS-30 | DR-3A-206 | 360 | 150
B-014 | 60 | WS-34 | SAW-30-160-252 | 540 | 150
B-014 | 20 | WS-37 | SAW-50-422 | 120 | 150
B-014 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-014 | 70 | WS-44 | FIN-GOOD-INV | 0 | 150
B-015 | 30 | WS-11 | TUR-40-100-404 | 600 | 150
B-015 | 40 | WS-21 | MIL-U1-605 | 540 | 150
B-015 | 50 | WS-30 | DR-3A-206 | 420 | 150
B-015 | 60 | WS-34 | SAW-30-160-252 | 480 | 150
B-015 | 20 | WS-37 | SAW-50-422 | 120 | 150
B-015 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-015 | 70 | WS-44 | FIN-GOOD-INV | 0 | 150
B-016 | 30 | WS-08 | MIL-10-150-401 | 600 | 150
B-016 | 40 | WS-20 | MIL-H21-604 | 1020 | 150
B-016 | 50 | WS-26 | DR-2A2-202 | 420 | 150
B-016 | 60 | WS-32 | SAW-30-150-251 | 420 | 150
B-016 | 20 | WS-36 | SAW-10-421 | 120 | 150
B-016 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-016 | 80 | WS-44 | FIN-GOOD-INV | 0 | 150
B-016 | 70 | WS-42 | TEMP-A01-202 | 720 | 150
B-017 | 30 | WS-13 | TUR-6-Sp1-406 | 540 | 150
B-017 | 40 | WS-22 | MIL-H2-606 | 480 | 150
B-017 | 50 | WS-30 | DR-3A-206 | 360 | 150
B-017 | 60 | WS-34 | SAW-30-160-252 | 480 | 150
B-017 | 20 | WS-37 | SAW-50-422 | 120 | 150
B-017 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-017 | 70 | WS-44 | FIN-GOOD-INV | 0 | 150

## Slide 8: Tables – Operations (cont´d)
Item ID | OP | Work Station | WS Type | Execution Time [s] | Lot Size
B-018 | 30 | WS-05 | MIL-A2-365 | 780 | 150
B-018 | 40 | WS-25 | DR-2A-201 | 480 | 150
B-018 | 50 | WS-27 | GR-T1-203 | 420 | 150
B-018 | 60 | WS-32 | SAW-30-150-251 | 600 | 150
B-018 | 20 | WS-02 | TUR-B2-362 | 120 | 150
B-018 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-018 | 70 | WS-42 | TEMP-A01-202 | 480 | 150
B-018 | 80 | WS-44 | FIN-GOOD-INV | 0 | 
B-019 | 30 | WS-08 | MIL-10-150-401 | 780 | 150
B-019 | 40 | WS-20 | MIL-H21-604 | 840 | 150
B-019 | 50 | WS-26 | DR-2A2-202 | 360 | 150
B-019 | 60 | WS-32 | SAW-30-150-251 | 720 | 150
B-019 | 20 | WS-36 | SAW-10-421 | 180 | 150
B-019 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-019 | 70 | WS-42 | TEMP-A01-202 | 720 | 150
B-019 | 80 | WS-44 | FIN-GOOD-INV | 0 | 150
B-020 | 30 | WS-05 | MIL-A2-365 | 960 | 150
B-020 | 40 | WS-22 | MIL-H2-606 | 720 | 150
B-020 | 50 | WS-30 | DR-3A-206 | 360 | 150
B-020 | 60 | WS-34 | SAW-30-160-252 | 660 | 150
B-020 | 20 | WS-38 | SAW-150-423 | 180 | 150
B-020 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-020 | 70 | WS-44 | FIN-GOOD-INV | 0 | 150
B-021 | 30 | WS-04 | TUR-A4-364 | 780 | 150
B-021 | 40 | WS-24 | MIL-V5-608 | 720 | 150
B-021 | 50 | WS-30 | DR-3A-206 | 420 | 150
B-021 | 60 | WS-35 | SAW-35-100-254 | 720 | 150
B-021 | 20 | WS-38 | SAW-150-423 | 180 | 150
B-021 | 70 | WS-42 | TEMP-A01-202 | 300 | 150
B-021 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-021 | 80 | WS-44 | FIN-GOOD-INV | 0 | 150
B-022 | 30 | WS-05 | MIL-A2-365 | 900 | 150
B-022 | 40 | WS-25 | DR-2A-201 | 480 | 150
B-022 | 50 | WS-27 | GR-T1-203 | 360 | 150
B-022 | 60 | WS-32 | SAW-30-150-251 | 720 | 150
B-022 | 20 | WS-02 | TUR-B2-362 | 240 | 150
B-022 | 70 | WS-42 | TEMP-A01-202 | 300 | 150
B-022 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-022 | 80 | WS-44 | FIN-GOOD-INV | 0 | 150
B-023 | 30 | WS-15 | TUR-6-Sp3-408 | 240 | 150
B-023 | 40 | WS-28 | DR-T3-204 | 300 | 150
B-023 | 20 | WS-41 | SAW-CNC-60-425 | 60 | 150
B-023 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-023 | 50 | WS-44 | FIN-GOOD-INV | 0 | 150
B-024 | 30 | WS-05 | MIL-A2-365 | 360 | 150
B-024 | 40 | WS-25 | DR-2A-201 | 300 | 150
B-024 | 20 | WS-02 | TUR-B2-362 | 60 | 150
B-024 | 10 | WS-43 | RAW-MAT-INV | 0 | 150
B-024 | 50 | WS-27 | GR-T1-203 | 120 | 150
B-024 | 60 | WS-32 | SAW-30-150-251 | 240 | 150
B-024 | 80 | WS-44 | FIN-GOOD-INV | 0 | 150
B-024 | 70 | WS-42 | TEMP-A01-202 | 480 | 150

## Slide 9: Benefit-Value Analysis
Benefit-Value Table |  |  |  |  |  |  |  |  | 
 |  |  |  | Option 1 |  | Option 2 |  | Option 3 | 
Criteria Category | Overall Weight | Criteria | Individual Weight Wi | Score | Benefit Value | Score | Benefit Value | Score | Benefit Value

## Slide 10: Production Morphology
# | Characteristics | Attributes |  |  |  |  | 
1 | Order Placement | Manufacturing based on individual orders | Manufacturing based on blanket orders |  | Anonymous pre-manufacturing w/ customized finishing |  | Make to stock
2 | Product spectrum | Products according to customer specification | Standardized products w/ customer specific versions |  | Standard products w/ versions |  | Standard products w/o versions
3 | Product structure | Multi-part products w/ complex structure |  | Multi-part products w/ simple structure |  | Products w/ less parts | 
4 | Determination of Material Requirements | Demand-based | Order-based |  | Anticipatory |  | Consumption-based
5 | Determination of Dependent Requirements | Order-based |  | Order-based & periodic |  | periodic | 
6 | Procurement Type | Extensive external procurement |  | External procurment to a greater extent |  | Insignificant external procurement | 
7 | Inventory | none | Inventory of items at lower structural levels |  | Inventory of items at higher structural levels |  | Inventory of products
8 | Production Type | One-off production | Small-batch production |  | Series production |  | Mass production
9 | Way of Manufacturing | Job shop manufacturing | Manufacturing cell |  | Line manufacturing |  | Flow manufacturing
10 | Way of Assembly | On-site assembly | Assembly cell |  | Line assembly |  | Flow assembly
11 | Structure of Manufacturing | Manufacturing w/ a high degree of structuring |  | Manufacturing w/ a medium degree of structuring |  | Manufacturing w/ a low degree of structuring | 
12 | Change Requests | Extensive |  | Occasional |  | insignificant | 

## Slide 11: House of quality

## Slide 12: Bill of Materials
BOM LEVEL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LVL | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | BOM ID | PART NO | NAME / DESCRIPTION | QTY | MAKE/BUY | SUPPLIER | COST | Total Cost | Material | NOTES
 | • |  |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 4 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 5 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 6 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 8 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 9 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 10 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 11 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 12 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 13 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 14 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 15 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 17 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 18 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 19 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 20 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 21 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 22 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 23 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 24 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 25 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 26 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 27 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 28 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 29 |  |  |  |  |  |  |  |  | 
 | • |  |  |  |  |  |  |  |  | 30 |  |  |  |  |  |  |  |  | 

## Slide 13: ABC Analysis
Item ID | Item | Annual Output | Cum. Output | Share [%] | Cum. Share [%]
B-001 | Scooter 001 | 130,978 |  |  | 
B-002 | Scooter 002 | 10 |  |  | 
B-003 | Scooter 003 | 635 |  |  | 
B-004 | Scooter 004 | 102 |  |  | 
B-006 | Scooter 006 | 61,638 |  |  | 
B-007 | Scooter 007 | 56,016 |  |  | 
B-008 | Scooter 008 | 765 |  |  | 
B-009 | Scooter 009 | 5 |  |  | 
B-010 | Scooter 010 | 3,467 |  |  | 
B-011 | Scooter 011 | 12,456 |  |  | 
B-012 | Scooter 012 | 67,368 |  |  | 
B-013 | Scooter 013 | 1,111 |  |  | 
B-015 | Scooter 015 | 453 |  |  | 
B-016 | Scooter 016 | 104,397 |  |  | 
B-018 | Scooter 018 | 976 |  |  | 
B-019 | Scooter 019 | 1,167 |  |  | 
B-021 | Scooter 021 | 222 |  |  | 
B-022 | Scooter 022 | 2,343 |  |  | 
B-023 | Scooter 023 | 13 |  |  | 
B-024 | Scooter 024 | 2,211 |  |  | 

## Slide 14: Routing - initial
 | Operation |  |  |  |  |  |  | 
Item ID | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80

## Slide 15: Clustering
 | Inv | Sawing |  |  | Turning |  |  | Milling |  |  |  |  |  |  |  | Drilling |  |  |  | Grinding |  | Sawing |  |  | Temp | Inv
Item ID | WS-43 | WS-36 | WS-38 | WS-40 | WS-02 | WS-04 | WS-07 | WS-03 | WS-05 | WS-08 | WS-18 | WS-20 | WS-21 | WS-23 | WS-24 | WS-25 | WS-26 | WS-28 | WS-31 | WS-27 | WS-29 | WS-32 | WS-33 | WS-34 | WS-42 | WS-44

## Slide 16: Routing Clustered
 | Operation |  |  |  |  |  |  | 
Item ID | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80

## Slide 17: Material Selection
Material | Tensile Strength (MPa) | Yield Strength (MPa) | Young’s Modulus (Gpa) | Toughness MN m-3/2 | Density (t/m3) | Specific Gravity (Kg/m3) | Cost per ton (€/t)
Aluminium 6061 | 300 | 120 | 75 | 55 | 2.70 | 2.7 | 3200
Aluminium 4043 | 145 | 70 | 100 | 48 | 2.90 | 2.3 | 2500
Aluminium 5005 | 105 | 85 | 69 | 38 | 2.60 | 2.2 | 1600
Aluminium 6063 | 310 | 97 | 70 | 39 | 2.65 | 2.3 | 1900
Aluminium 7005 | 350 | 150 | 79 | 40 | 2.78 | 2.5 | 2200
 | Tensile Strength (MPa) | Yield Strength (MPa) | Young’s Modulus (Gpa) | Toughness MN m-3/2 | Density (t/m3) | Total | Normalized | Weighting factor
Tensile Strength (MPa) |  |  |  |  |  |  |  | 
Yield Strength (MPa) |  |  |  |  |  |  |  | 
Young’s Modulus (Gpa) |  |  |  |  |  |  |  | 
Toughness MN m-3/2 |  |  |  |  |  |  |  | 
Density (t/m3) |  |  |  |  |  |  |  | 
 | Scaled | Scaled | Scaled | Scaled | Scaled | 
 | Tensile Strength (MPa) | Yield Strength (MPa) | Young’s Modulus (Gpa) | Toughness MN m-3/2 | Density (t/m3) | Performance Index (γ)
Aluminium 6061 |  |  |  |  |  | 
Aluminium 4043 |  |  |  |  |  | 
Aluminium 5005 |  |  |  |  |  | 
Aluminium 6063 |  |  |  |  |  | 
Aluminium 7005 |  |  |  |  |  | 
Material Properties
Material Properties Weights
Material Performance Index

## Slide 18: Material Selection (Cont´d)
Scaled Properties | Relative Cost b | Levelized Cost of Unit Strength (€/Nm) | Performance Index (γ) | Figure of merit
Aluminium 6061 |  |  |  | 
Aluminium 4043 |  |  |  | 
Aluminium 5005 |  |  |  | 
Aluminium 6063 |  |  |  | 
Aluminium 7005 |  |  |  | 
Safety Factor Working Stress | 3 |  |  |  | 
Material | Yield Strength (MPa) | Working Stress (MPa) | Specific Gravity (Kg/m3) | Relative Cost b | Cost of Unit Strength (€/Nm)
Aluminium 6061 |  |  |  |  | 
Aluminium 4043 |  |  |  |  | 
Aluminium 5005 |  |  |  |  | 
Aluminium 6063 |  |  |  |  | 
Aluminium 7005 |  |  |  |  | 
Material Cost per Unit Strength
Material Figure of Merit